Tau mutant EMMI simulation Protocol

1. Making Mutations (PyMOL mutagenesis)

2. Preparation Simulation

gmx pdb2gmx -f S262D_HIS_2.pdb -o S262D.gro -water tip3p -ignh

gmx editconf -f S262D.gro -o S262D_box.gro -center 4.33 4.5 36.00 -box 10.5 12.5 67.0
>>(worked in 07.06 experiment)

gmx solvate -cp S262D_box.gro -cs spc216.gro -o S262D_solv.gro -p topol.top
> > tip3p.gro is not in GROMACS. Google says spc216.gro is compatible with tip3p.gro

gmx grompp -f ions.mdp -c S262D_solv.gro -p topol.top -o ions.tpr -maxwarn 2

<ions.mdp>
; minim.mdp - used as input into grompp to generate em.tpr
; Parameters describing what to do, when to stop and what to save
integrator = steep ; Algorithm (steep = steepest descent minimization)
emtol = 100.0 ; Stop minimization when the maximum force < 500.0 kJ/mol/nm
emstep = 0.002 ; Minimization step size
nsteps = 5000000 ; Maximum number of (minimization) steps to perform
energygrps	= system	; Which energy group(s) to write to disk

; Parameters describing how to find the neighbors of each atom and how to calculate the interactions
nstlist = 10 ; Frequency to update the neighbor list and long range forces
cutoff-scheme = Verlet ; Buffered neighbor searching
ns_type = grid ; Method to determine neighbor list (simple, grid)
coulombtype = PME ; Treatment of long range electrostatic interactions
rcoulomb = 1.0 ; Short-range electrostatic cut-off
rvdw = 1.0 ; Short-range Van der Waals cut-off
pbc = xyz ; Periodic Boundary Conditions in all 3 dimensions

gmx genion -s ions.tpr -o S262D_ionized.gro -p topol.top -pname NA -nname CL -neutral

<EM>
gmx grompp -f em.mdp -c S262D_ionized.gro -p topol.top -o em.tpr
(em.mdp parameters are same as ions.mdp)

gmx mdrun -v -deffnm em

gmx energy -f em.edr -o potential.xvg

<NPT>
gmx grompp -f npt.mdp -c em.gro -p topol.top -r em.gro -o npt.tpr -maxwarn 2

<npt.mdp>
title = NPT Equilibration
define = -DPOSRES ; position restrain the protein
; Run parameters
integrator = md ; leap-frog integrator
nsteps = 150000 ; 0.002 * 250000 = 300 ps
dt = 0.002 ; [ps] 2 fs
; Output control
nstxout = 100 ; save coordinates every 0.2 ps
nstvout = 100 ; save velocities every 0.2 ps
nstenergy = 100 ; save energies every 0.2 ps
nstlog = 100 ; update log file every 0.2 ps

; COM motion removal
; These options remove COM motion of the system
nstcomm = 100
nstcalcenergy = 100
comm-mode = Linear
comm-grps = System

; Bond parameters
continuation = no ; Initial simulation
constraint_algorithm = lincs ; holonomic constraints
constraints = h-bonds ; all bonds (even heavy atom-H bonds) constrained
lincs_iter = 1 ; accuracy of LINCS
lincs_order = 4 ; also related to accuracy

; Neighborsearching
cutoff-scheme = Verlet ; Verlet: particle based cut-offs, group: using charge groups
ns_type = grid ; search neighboring grid cels
nstlist = 5 ; was 10 in tutorial, 5(10fs) in the paper
rlist = 1.0 ; short-range neighborlist(=pairlist) cutoff (in nm)
rcoulomb = 1.0 ; short-range electrostatic cutoff (in nm)
rvdw = 1.0 ; short-range van der Waals cutoff (in nm)

; Electrostatics
coulombtype = PME ; Particle Mesh Ewald for long-range electrostatics
pme_order = 4 ; cubic interpolation(same as tutorial)
fourierspacing = 0.12 ; grid spacing for FFT

; Temperature coupling is on
tcoupl = V-rescale ; Weak coupling for initial equilibration
tc-grps = Protein Non-Protein ; two coupling groups - more accurate
tau_t = 0.2 0.2 ; [ps] time constant (tutorial used 0.1)
ref_t = 310 310 ; reference temperature, one for each group, in K

; Pressure coupling is on
pcoupl = Parrinello-Rahman ; Pressure coupling (warning suggested Berendsen)
pcoupltype = isotropic ; uniform scaling of x-y-z box vectors
tau_p = 1.0 ; time constant, in ps (tutorial used 2)
ref_p = 1.0 ; reference pressure (in bar)
compressibility = 4.5e-5 ; isothermal compressibility, bar^-1
refcoord_scaling = com

; Periodic boundary conditions
pbc = xyz ; 3-D PBC

; Dispersion correction
DispCorr = EnerPres ; account for cut-off vdW scheme

; Velocity generation
gen_vel = yes ; Velocity generation is on
gen_temp = 310 ; temperature for velocity generation
gen_seed = -1 ; random seed

gmx mdrun -deffnm npt

gmx energy -f npt.edr -o potential.xvg

gmx energy -f npt.edr -o pressure.xvg

<NPT>
gmx grompp -f nvt.mdp -c npt.gro -r npt.gro -t npt.cpt -p topol.top -o nvt.tpr
<nvt.mdp>

title = NPT Equilibration
define = -DPOSRES ; position restrain the protein
; Run parameters
integrator = md ; leap-frog integrator
nsteps = 500000 ; 0.002 * 250000 = 1000 ps (2ns)
dt = 0.002 ; [ps] 2 fs
; Output control
nstxout = 100 ; save coordinates every 0.2 ps
nstvout = 100 ; save velocities every 0.2 ps
nstenergy = 100 ; save energies every 0.2 ps
nstlog = 100 ; update log file every 0.2 ps

; COM motion removal
; These options remove COM motion of the system
nstcomm = 100
nstcalcenergy = 100
comm-mode = Linear
comm-grps = System

; Bond parameters
continuation = yes ; Restarting after NVT
constraint_algorithm = lincs ; holonomic constraints
constraints = h-bonds ; all bonds (even heavy atom-H bonds) constrained
lincs_iter = 1 ; accuracy of LINCS
lincs_order = 4 ; also related to accuracy

; Neighborsearching
cutoff-scheme = Verlet ; Verlet: particle based cut-offs, group: using charge groups
ns_type = grid ; search neighboring grid cels
nstlist = 5 ; was 10 in tutorial, 5(10fs) in the paper
rlist = 1.0 ; short-range neighborlist(=pairlist) cutoff (in nm)
rcoulomb = 1.0 ; short-range electrostatic cutoff (in nm)
rvdw = 1.0 ; short-range van der Waals cutoff (in nm)

; Electrostatics
coulombtype = PME ; Particle Mesh Ewald for long-range electrostatics
pme_order = 4 ; cubic interpolation(same as tutorial)
fourierspacing = 0.12 ; grid spacing for FFT

; Temperature coupling is on
tcoupl = V-rescale ; Weak coupling for initial equilibration
tc-grps = Protein Non-Protein ; two coupling groups - more accurate
tau_t = 0.2 0.2 ; [ps] time constant (tutorial used 0.1)
ref_t = 310 310 ; reference temperature, one for each group, in K

; Pressure coupling is off
pcoupl = no ; Pressure coupling (warning suggested Berendsen)

; Periodic boundary conditions
pbc = xyz ; 3-D PBC

; Dispersion correction
DispCorr = EnerPres ; account for cut-off vdW scheme

; Velocity generation
gen_vel = no ; Velocity generation is off

gmx mdrun -deffnm nvt

<For counting number of frames>
gmx dump -f nvt.trr | grep "^frame" | wc -l

gmx check -f file.trr

gmx energy -f nvt.edr -o potential.xvg

gmx energy -f nvt.edr -o temperature.xvg

3. EMMI

<Preparing nvt_prod.mdp>

title = NPT Equilibration
define = -DPOSRES ; position restrain the protein
; Run parameters
integrator = md ; leap-frog integrator
nsteps = 50000000 ; 0.002 * 50000000 = 100 ns
dt = 0.002 ; [ps] 2 fs
; Output control
nstxout = 2500 ; save coordinates every 5 ps
nstvout = 0 ; save velocities every 0 ps
nstenergy = 2500 ; save energies every 5 ps
nstlog = 2500 ; update log file every 5 ps

; COM motion removal
; These options remove COM motion of the system
nstcomm = 100
nstcalcenergy = 100
comm-mode = Linear
comm-grps = System

; Bond parameters
continuation = no ; Restarting after NVT
constraint_algorithm = lincs ; holonomic constraints
constraints = h-bonds ; H bonds constrained
lincs_iter = 1 ; accuracy of LINCS
lincs_order = 4 ; also related to accuracy

; Neighborsearching
cutoff-scheme = Verlet ; Verlet: particle based cut-offs, group: using charge groups
ns_type = grid ; search neighboring grid cels
nstlist = 5 ; was 10 in tutorial, 5(10fs) in the paper
rlist = 1.0 ; short-range neighborlist(=pairlist) cutoff (in nm)
rcoulomb = 1.0 ; short-range electrostatic cutoff (in nm)
rvdw = 1.0 ; short-range van der Waals cutoff (in nm)

; Electrostatics
coulombtype = PME ; Particle Mesh Ewald for long-range electrostatics
pme_order = 4 ; cubic interpolation(same as tutorial)
fourierspacing = 0.12 ; grid spacing for FFT

; Temperature coupling is on
tcoupl = V-rescale ; Weak coupling for initial equilibration
tc-grps = Protein Non-Protein ; two coupling groups - more accurate
tau_t = 0.2 0.2 ; [ps] time constant (tutorial used 0.1)
ref_t = 310 310 ; reference temperature, one for each group, in K

; Pressure coupling is off
pcoupl = no ; Pressure coupling (warning suggested Berendsen)

; Periodic boundary conditions
pbc = xyz ; 3-D PBC

; Dispersion correction
DispCorr = EnerPres ; account for cut-off vdW scheme

; Velocity generation
gen_vel = no ; Velocity generation is off

<Making plumed.dat file>
RESTART

MOLINFO STRUCTURE=S262D_HIS_2.pdb
# define all heavy atoms using GROMACS index file
# which can be created with gmx_mpi make_ndx
protein-h: GROUP NDX_FILE=index_08.01.ndx NDX_GROUP=Protein-H
protein: GROUP NDX_FILE=index_08.01.ndx NDX_GROUP=Protein
system: GROUP NDX_FILE=index_08.01.ndx NDX_GROUP=System

# create EMMI score (defined as gmm)
# this part seems straight forward. Consistent with most of the EMMI files.
# NL_stride,NL_cutoff = paper: neighborlists are updated every 100 steps with cutoff equal to 0.01

EMMI ...
LABEL=gmm NOPBC TEMP=310.0 NL_STRIDE=100 NL_CUTOFF=0.01
ATOMS=protein-h GMM_FILE=MT_TAU.dat
SIGMA_MIN=0.03 RESOLUTION=0.1 NOISETYPE=MARGINAL

#ATOMS selects what is refined
# no-negative-no-h or no-h are reasonable
# resolution is not used - no Bfactor fitting
# SIGMA_MIN can go down to 0.02, must be > NL_CUTOFF, if crashes, raise back to 0.05,

# the larger the number the softer the contribution of the EM data

#WRITE_OV=OV_FILE.dat
#WRITE_OV_STRIDE=500
...

# translate into bias (ARG = gmm that we defined above)
# paper: cryo-EM restraints was calculated every 2MD steps
emr: BIASVALUE ARG=gmm.scoreb STRIDE=2

#DUMPMASSCHARGE FILE=mcfile
# print useful info to file
PRINT ARG=* FILE=COLVAR STRIDE=5000

<Making .ndx file>
>> Use the indexmaker.ipynb to extract the heavy atom indices from the pdb file.

gmx make_ndx -f conf0.gro -o index.ndx
>>copy paste heavy atom indices in this index.ndx file.

<Making Folders for each Parallel simulation>
for i in `seq 0 11`; do j=`printf "%02d\n" $i`; mkdir rep-${j}; done
for i in `seq 0 5`; do j=`printf "%02d\n" $i`; mkdir rep-${j}; done

<Extracting frames from previous NPT simulation>
echo 0 | gmx trjconv -f ../nvt/nvt.trr -s ../nvt/nvt.tpr -sep -o conf.gro -dt 166
echo 0 | gmx trjconv -f ../nvt/nvt.trr -s ../nvt/nvt.tpr -sep -o conf.gro -dt 333
>>2000ps/12 = 166.6667ps
>>2000ps/6 = 333.3333ps

<Making topol.tpr in each Folder and copy pasting index.ndx>

# create tpr file
>> before this command make sure your big folder has posre.itp, topop.top
for i in `seq 0 5`
do
 j=`printf "%02d\n" $i`
 gmx grompp -f nvt_prod.mdp -c conf${i}.gro -r conf${i}.gro -n index_08.01.ndx -o rep-${j}/topol.tpr
 cp plumed.dat rep-${j}
done
>> if plumed.dat file is not moved to each folder, do it manually
>> also copy paste the pdb, ndx, MT_TAU file to each folder

<Run>

set number threads you’re gonna use, check omp_num_threads
export OMP_NUM_THREADS=2 (THREADS is not number of cores. Np * ntomp should not exceed the number of CPU cores (12))
echo $OMP_NUM_THREADS

mpiexec -np 12 --oversubscribe gmx_mpi mdrun -multidir rep-* -pin on -ntomp $OMP_NUM_THREADS -plumed plumed.dat -cpi -noappend
mpiexec -np 6 --oversubscribe gmx_mpi mdrun -multidir rep-* -pin on -ntomp $OMP_NUM_THREADS -plumed plumed.dat -cpi -noappend